## Slide 1
Contact ANTIX to create your solution
ANTIX
shenzhenANTIX
Precision solutions for all displays
OUTDOOR | INDOOR | FLEXIBLE
We tailor modules to your unique specs
Technology co., Ltd

## Slide 2
01 02 |  |  | 03 04 05 06 |  |  |  |  | 
Dual |  | Flexible | GOB LED | COB LED |  | Indoor LED |  | Outdoor
Service LED Module |  | LED Module | Module | Module |  | Module |  | LED Module PART 06
PART 01 |  | PART 02 | PART 03 | PART 04 |  | PART 05 |  | 

## Slide 3
ANTIX
Dual Service LED Module
01
PART ONE

## Slide 4
Front And Rear Service 01
LED Display Module
01 HIGH REFRESH RATE
02 SMD 3 in 1
03 2 YEARS WARRANTY

## Slide 5
LED Chips
Easy Assembling
Dual Service LED 01
Screen Panel
The front and rear service LED module can be replaced or taken out from the front side or real side easily by only one person . No screws design, so it is easier to mount the modules on the cabinet quickly.
Dual-mode
maintenance (Front
& Rear) outdoor LED
display panel ,
saving the
maintenance space
and being compatible
with hard installation
conditions.
W e c h o o s e h i g h quality L E D c hi ps such as Nationstar, Kinglight for outdoor front& rear service L E D m o d u l e s , ensuring high refresh rate w it h t he best color uniformity.
Adopting high reliable
SMD1921, SMD2727
and SMD3535 to
ensure outdoor
front&rear access
LED modules perform
high brightness from
5500 – 7500 CD/㎡ .
SMD 3 in 1 LED
Dual-mode Maintenancm

## Slide 6
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P4 | SMD1921 | 320*320 | 80*80 | 1/ 10 | 3840 | 5500
P5 | SMD1921 | 320*320 | 64*64 | 1/8 | 3840 | 5000
P5.33 | SMD1921 | 320*320 | 60*60 | 1/8 | 3840 | 5000
P6.67 | SMD2727 | 320*320 | 48*48 | 1/6 | 3840 | 5500
P8 | SMD3535 | 320*320 | 40*40 | 1/5 | 3840 | 5000
P10 | SMD3535 | 320*320 | 32*32 | 1/2 | 3840 | 6000
P10-DIP | DIP346 | 320*320 | 32*32 | 1/4 | 3840 | 9000
320x320mm Dual Service (Frontal & Rear) 01 Outdoor LED Module

## Slide 7
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P3.12 | SMD1415 | 250*250 | 80*80 | 1/ 10 | 3840 | 6500
P3.91 | SMD1921 | 250*250 | 64*64 | 1/8 | 3840 | 6000
P4.81 | SMD1921 | 250*250 | 52*52 | 1/6 | 3840 | 5500
P5.95 | SMD2727 | 250*250 | 42*42 | 1/7 | 3840 | 6000
P6.94 | SMD2727 | 250*250 | 36*36 | 1/6 | 3840 | 6000
P8.33 | SMD3535 | 250*250 | 30*30 | 1/5 | 3840 | 6000
P10.41 | SMD3535 | 250*250 | 24*24 | 1/2 | 3840 | 6000
250x250mm Dual Service (Frontal & Rear) 01 Outdoor LED Module

## Slide 8
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P3.07 | SMD1415 | 320*160 | 104*52 | 1/13 | 3840 | 5500
P4 | SMD1921 | 320*160 | 80*40 | 1/ 10 | 3840 | 5500
P5 | SMD1921 | 320*160 | 64*32 | 1/8 | 3840 | 5500
P6.67 | SMD2727 | 320*160 | 48*24 | 1/6 | 3840 | 5500
P8 | SMD2727 | 320*160 | 40*20 | 1/5 | 3840 | 5000
P10 | SMD2727 | 320*160 | 32* 16 | 1/2 | 3840 | 6000
320x160mm Dual Service (Frontal & Rear) 01 Outdoor LED Module

## Slide 9
ANTIX
Flexible LED
Module
02
PART T O

## Slide 10
Flexible Soft LED 02
Display Module
The main feature of Flexible LED Screen Panel is that the LED panel is soft, flexible.
Compare to indoor fixed LED display and outdoor fixed LED display, the flexible LED panel can be any designed forrolled, bend and swing to do any shape LED video wall as you want.
Super flexible Soft LED display module with high-quality driving IC and LEDs with high refresh rate and
great color uniformity.
We offer various pixels for flexible LED panel ranges from P1.875mm, P2mm, P3mm, P4mm to P5mm.
The panel sizes can be 240*120mm, 320mm* 160mm and 256*128mm.

## Slide 11
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P0.9 | COB | 240*120 | 256*128 | 1/64 | 3840 | 800
P0.9 | IMD-M09 | 240*120 | 256*128 | 1/64 | 3840 | 650
P1.25 | SMD1010 | 240*120 | 192*96 | 1/48 | 3840 | 650
P1.579 | SMD1212 | 240*120 | 152*76 | 1/38 | 3840 | 700
P1.875 | SMD1515 | 240*120 | 128*64 | 1/32 | 3840 | 700
P2 | SMD1515 | 240*120 | 120*60 | 1/30 | 3840 | 700
P2.5 | SMD1515 | 240*120 | 96*48 | 1/24 | 3840 | 700
P3 | SMD2020 | 240*120 | 80*40 | 1/20 | 3840 | 650
P4 | SMD2020 | 240*120 | 60*30 | 1/ 15 | 3840 | 650
240x120mm Series Flexible Soft LED LED 02
Display Module

## Slide 12
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P1.25 | SMD1010 | 320*160 | 256*128 | 1/64 | 3840 | 600
P1.29 | SMD1010 | 320*160 | 248*124 | 1/62 | 3840 | 600
P1.53 | SMD1212 | 320*160 | 208*104 | 1/52 | 3840 | 600
P1.56 | SMD1212 | 320*160 | 204* 102 | 1/51 | 3840 | 600
P1.86 | SMD1212 | 320*160 | 172*86 | 1/43 | 3840 | 600
P2 | SMD1515 | 320*160 | 160*80 | 1/40 | 3840 | 650
P2.5 | SMD1515 | 320*160 | 128*64 | 1/32 | 3840 | 700
P3.076 | SMD2020 | 320*160 | 104*52 | 1/26 | 3840 | 700
P4 | SMD2020 | 320*160 | 80*40 | 1/20 | 3840 | 600
P5 | SMD2020 | 320*160 | 64*32 | 1/ 16 | 3840 | 600
320x160mm Series Flexible Soft LED 02
Screen Module

## Slide 13
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P1.56 | SMD1212 | 200*150 | 128*96 | 1/48 | 3840 | 700
P2 | SMD1515 | 256*128 | 128*64 | 1/32 | 3840 | 800
P4 | SMD2020 | 256*128 | 64*32 | 1/ 16 | 3840 | 700
256x128mm & 200x150mm Series Flexible 02 Soft LED Display Module

## Slide 14
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P1.56 | SMD1212 | 250*250 | 160*160 | 1/40 | 3840 | 600
P1.95 | SMD1515 | 250*250 | 128*128 | 1/32 | 3840 | 700
P2.6 | SMD1515 | 250*250 | 96*96 | 1/32 | 3840 | 700
250x250mm Series Flexible Soft LED 02
Display Module

## Slide 15
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P1.2 | SMD1010 | 300*168.75 | 240*135 | 1/45 | 3840 | 600
P1.5 | SMD1212 | 300*168.75 | 192* 108 | 1/54 | 3840 | 600
P1.8 | SMD1515 | 300*168.75 | 160*90 | 1/45 | 3840 | 700
P2.3 | SMD1515 | 300*168.75 | 128*72 | 1/36 | 3840 | 700
300×168.75mm Series Flexible Soft LED 02
Display Module

## Slide 16
ANTIX
PART THREE
GOB LED
Module
03

## Slide 17
GOB LED Display Module
High Waterproof Level
With the innovative glue-filled seal on the surface of the module. it can well protect the LED on the LED module from water.
Use advanced new material to cover the lamp surface to provide effective protection. the Ultra-high waterproof level is IP68.
03

## Slide 18
GOB LED Display 03
Module
High Dust-Proof Level
With high sealing performance of new material , the GOB LED screen panel is totally dust-free with excellent clarity,
and offers excellent visual effecrt with high refresh rate and uniformity color.
High Shockproof Level
Special-designing dash-proof glue able to have shock-proof function, offering ultra high protection for LEDs in the various impacts.

## Slide 19
Excellent Visual Performance
The new material glue does not only has ultra- high transparency but also has excellent thermal conductivity.
Compared with traditional LED modules . GOB LED modules can also provide lifelike colors and a visual appearance.
Can Used for Flexible LED Panel
GOB technology can not only be used for traditional LED display modules but also can be applied to the LED soft module.
This feature can perfectly protect soft LEDs as soft LED panels don’t have masks.
GOB LED Display 03
Module

## Slide 20
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P1.25 | SMD1010 (Black LED) | 320*160 | 256*128 | 1/32 | 3840 | 600
P1.53 | SMD1212 (Black LED) | 320*160 | 208*104 | 1/26 | 3840 | 600
P1.86 | SMD1515 (Black LED) | 320*160 | 172*86 | 1/43 | 3840 | 600
P2 | SMD1515 (Black LED) | 320*160 | 160*80 | 1/40 | 3840 | 700
P2.5 | SMD2020 (Black LED) | 320*160 | 128*64 | 1/32 | 3840 | 800
P3.076 | SMD2020 (Black LED) | 320*160 | 104*52 | 1/26 | 3840 | 800
320x160mm Series GOB LED Screen Panel 03

## Slide 21
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P1.56 | SMD1212 (Black LED) | 250*250 | 160*160 | 1/40 | 3840 | 750
P1.95 | SMD1515 (Black LED) | 250*250 | 128*128 | 1/32 | 3840 | 800
P2.5 | SMD1515 (Black LED) | 250*250 | 100*100 | 1/25 | 3840 | 800
P2.6 | SMD1515 (Black LED) | 250*250 | 96*96 | 1/32 | 3840 | 750
250x250mm Series GOB LED Display Panel 03

## Slide 22
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P2 | SMD1515 (Black LED) | 256*128 | 128*64 | 1/32 | 3840 | 800
P2.5 | SMD2020 (Black LED) | 160*160 | 64*64 | 1/32 | 3840 | 800
P3 | SMD2020 (Black LED) | 192* 192 | 64*64 | 1/32 | 3840 | 700
Other Series GOB LED Screen Module 03

## Slide 23
ANTIX
PART FOUR
COB LED
Module
04

## Slide 24
COB LED Display Module 04
COB LED display module, as an LED module using
COB (Chip on Board) packaging technology, has 发展规划
greater advantages in display effect , stability and protection . The LED screen displays more delicate pictures . For example , COB display used for high- end conference room display, when watching high- definition images at close range , the picture is still clear and smooth.

## Slide 25
Unlike traditional SMD surface-mount packaging, COB packaging technology integrates light-emitting chips into PCB
boards instead of soldering them one by one on PCB. This packaging method not only simplifies the production
process, but also significantly improves the overall performance of the display. COB packaging technology is generally
divided into COB flip-chip and COB front-mount. Compared with traditional front-mount technology, COB flip-chip
presents unique characteristics in appearance, size, heat dissipation performance, etc.
COB Packaging Technology 04
Front-mounted COB
Flip-chip COB

## Slide 26
Excellent Display Effect 04

## Slide 27
COB technology significantly reduces the package size of LED modules . This not only improves the overall performance and reliability of LED displays, but also makes LED displays lighter, easier to install and maintain.
COB LED modules have a higher protection level, good waterproof and moisture-proof performance, and a smooth and hard surface , which is anti- collision and anti-bump.
Stability and Protection 04

## Slide 28
High Definition 04
COB LED modules do not have the lamp bead structure in traditional SMD packages, achieving smaller pixel pitch. The pixel pitch of COB display screens is usually below 2.0mm, such as P0.62, P0.78, P0.93, P1.25, and P1.53, which has incomparable advantages in the field of ultra-high-definition display. Smaller dot pitch means higher pixel density and finer image performance, which can meet the audience’s demand for high-definition picture quality.

## Slide 29
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P1.25 | Flip chip COB | 320*160 | 256*128 | 1/64 | 3840 | 600
P1.53 | Flip chip COB | 320*160 | 208*104 | 1/52 | 3840 | 600
P1.86 | Flip chip COB | 320*160 | 172*86 | 1/43 | 3840 | 600
320x160mm Series COB LED Display Module 04

## Slide 30
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P0.62 | Flip chip COB | 150*168.75 | 242*272 | 1/64 | 3840 | 500-800
P0.78 | Flip chip COB | 150*168.75 | 192*216 | 1/64 | 3840 | 500-800
P0.93 | Flip chip COB | 150*168.75 | 160*180 | 1/60 | 3840 | 500-800
P1.25 | Flip chip COB | 150*168.75 | 120*135 | 1/60 | 3840 | 500-800
P1.56 | Flip chip COB | 150*168.75 | 96*108 | 1/54 | 3840 | 500-800
P1.87 | Flip chip COB | 150*168.75 | 80*90 | 1/45 | 3840 | 500-800
150×168.75mm Series COB LED Display Module 04

## Slide 31
PART F VE
Indoor LED
Module
05
ANTIX

## Slide 32
High Refresh rate indoor LED Screen Panel , High quality full color SMD indoor LED display module Including the Data Power Cables and 2 Years Warranty,
All LED modules With Best Contrast and Color uniformity to ensure the LED display has excellent visual effect.
Indoor LED Display Module 05
发展规划
DEV飞OPMENT

## Slide 33
IC Driver
For indoor LED display
modules, we choose High-
Quality
Nationstar/Kinglight/Hongs
en LEDs from LED Lamps
Factory directly which have
high color contrast and
best color uniformity so as
to meet the need for high
grayscale and keeping
natural color.
Eagerled Indoor LED
display Panel has all pixel
available from P2mm,
P2.5mm, P3mm,
P3.91mm, P4mm,
P4.81mm, P5mm, P6mm,
P7.72mm, P10mm and
small pixel series such as
P1.875mm , P1.25mm,
P1.538mm, P1.667mm,
P1.86mm, etc
7 2 Hours agi ng test (white balance aging (2×24 hours) and video aging ( 2 4 hours ) ) to improve the reliability the indoor LED display modules and ensure the LED modules without broken leds.
To achieve the best visual pe rfo r ma n ce of L i n s n indoor LED display panel , we use the best Driving IC, such as MIB5153,MBI5124, ICN2153 , ICN2038S with high refresh rate and high grey level with the latest technologies.
Indoor LED Screen Panel 05
72+ Hours Aging Tests
LED Lamps
Various Pixel Pitch Avaliable

## Slide 34
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P1.25 | SMD1010 | 320*160 | 256*128 | 1/64 | 3840 | 600
P1.53 | SMD1212 | 320*160 | 208*104 | 1/52 | 3840 | 600
P1.86 | SMD1515 | 320*160 | 172*86 | 1/43 | 3840 | 600
P2 | SMD1515 | 320*160 | 160*80 | 1/40 | 3840 | 700
P2.5 | SMD2020 | 320*160 | 128*64 | 1/32 | 3840 | 800
P3.076 | SMD2020 | 320*160 | 104*52 | 1/26 | 3840 | 800
P4 | SMD2020 | 320*160 | 80*40 | 1/20 | 3840 | 700
320x160mm Series Indoor LED Module 05

## Slide 35
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P1.56 GOB | SMD1212 | 250*250 | 160*160 | 1/40 | 3840 | 750
P1.95 GOB | SMD1515 | 250*250 | 128*128 | 1/32 | 3840 | 800
P2.6 GOB | SMD1515 | 250*250 | 96*96 | 1/32 | 3840 | 750
P2.97 | SMD2020 | 250*250 | 84*84 | 1/28 | 3840 | 800
P3.91 | SMD2020 | 250*250 | 64*64 | 1/ 16 | 3840 | 800
250x250mm Series Cable Connection 05
Indoor LED Module

## Slide 36
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P1.56 GOB | SMD1212 | 250*250 | 160*160 | 1/40 | 3840 | 750
P1.95 GOB | SMD1515 | 250*250 | 128*128 | 1/32 | 3840 | 800
P2.6 GOB | SMD1515 | 250*250 | 96*96 | 1/32 | 3840 | 750
P2.97 | SMD2020 | 250*250 | 84*84 | 1/28 | 3840 | 800
P3.91 | SMD2020 | 250*250 | 64*64 | 1/ 16 | 3840 | 700
250x250mm Series Hub Connection Indoor 05
LED Module

## Slide 37
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P1.95 GOB | SMD1515 | 250*250 | 128*128 | 1/32 | 3840 | 800
P2.6 GOB | SMD1515 | 250*250 | 96*96 | 1/32 | 3840 | 750
P2.97 | SMD2020 | 250*250 | 84*84 | 1/28 | 3840 | 800
P3.91 | SMD2020 | 250*250 | 64*64 | 1/ 16 | 3840 | 700
250x250mm Series Hub Connection Indoor 05 Flexible LED Module

## Slide 38
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P0.93 | MiniLED | 300*168.75 | 320*180 | 1/60 | 3840 | 300-800
P1.25 | SMD1010 | 300*168.75 | 240*135 | 1/60 | 3840 | 300-800
P1.56 | SMD1010 | 300*168.75 | 192* 108 | 1/64 | 3840 | 300-800
P1.87 | SMD1515 | 300*168.75 | 160*90 | 1/45 | 3840 | 300-800
P1.25 | SMD1010 | 320*180 | 256*144 | 1/60 | 3840 | 300-800
P1.53 | SMD1010 | 320*180 | 208*116 | 1/60 | 3840 | 300-800
P1.86 | SMD1010 | 320*180 | 172*96 | 1/64 | 3840 | 300-800
P1.25 | SMD1010 | 320*160 | 256*128 | 1/64 | 3840 | 600
P1.53 | SMD1010 | 320*160 | 208*104 | 1/52 | 3840 | 600
P1.86 | SMD1515 | 320*160 | 172*86 | 1/43 | 3840 | 600
P2 | SMD1515 | 320*160 | 160*80 | 1/40 | 3840 | 700
P2.5 | SMD2020 | 320*160 | 128*64 | 1/32 | 3840 | 800
Other Series Hub Connection Indoor LED Module 05

## Slide 39
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P2 | SMD1515 | 256*128 | 128*64 | 1/32 | 3840 | 800
P2.5 | SMD2020 | 160*160 | 64*64 | 1/32 | 3840 | 800
P3 | SMD2020 | 192* 192 | 64*64 | 1/32 | 3840 | 700
P4 | SMD2020 | 256*128 | 64*32 | 1/ 16 | 3840 | 800
P4 | SMD2020 | 256*256 | 64*64 | 1/32 | 3840 | 600
Other Series Indoor LED Display Modules 05

## Slide 40
PART SX
Outdoor
LED Module
06
ANTIX

## Slide 41
High quality full color SMD outdoor LED display module Including the Data Power Cables and 2 Years Warranty.
All LED modules With high brightness and Color uniformity to ensure the LED display has excellent visual effect.
Outdoor LED Display Module 06
发展规划
DEV飞OPMENT

## Slide 42
LED Lamps
72+ Hours Aging Tests
All pixel available including
P2.5mm,P3mm, P4mm,
P5mm, P3.91mm, P4.81mm,
P5mm, P6mm, P6.67mm,
P8mm, P10mm, and DIP
1R1G1B series such as
P10mm, P16mm, P20mm,
etc. Various sizes
320*160mm, 160mm* 160mm,
192mm* 192mm,250mmx250
mm and 256mm* 128mm are
in stock.
To achieve the best
visual performance of
outdoor LED display, we
use the best driving IC
such as
MBI5153,MBI5124,
ICN2153,ICN2038S
with high refresh rate
and high grey level with
the latest technologies.
We choose high-
quality LED chips
such as Nationstar,
Kinglight for outdoor
LED display modules.
Furthermore, high
brightness and IP65
waterproof protection
can be provided.
7 2 Hours agi ng test (white balance aging (2×24 hours) and video aging ( 2 4 hours ) ) to improve the reliability the outdoor LED display modules and ensure the LED modules without broken leds.
Outoor LED Screen Panel 06
IC Driver
Various Pixel Pitch Avaliable

## Slide 43
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P2.5 | SMD1415 | 320*160 | 128*64 | 1/ 16 | 3840 | 5000
P3.076 | SMD1415 | 320*160 | 104*52 | 1/ 13 | 3840 | 5000
P4 | SMD1921 | 320*160 | 80*40 | 1/ 10 | 3840 | 5500
P5 | SMD2727 | 320*160 | 64*32 | 1/8 | 3840 | 5500
P5 | SMD1921 | 320*160 | 64*32 | 1/8 | 3840 | 5500
P6.67 | SMD3535 | 320*160 | 48*24 | 1/6 | 3840 | 6000
P8 | SMD3535 | 320*160 | 40*20 | 1/5 | 3840 | 5500
P10 | SMD3535 | 320*160 | 32* 16 | 1/2 | 3840 | 5800
P10 | DIP346 1R1G1B | 320*160 | 32* 16 | 1/4 | 3840 | 8000
320x160mm Series Outdoor LED Display Module 06

## Slide 44
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P5 | SMD1921 | 320*160 | 64*32 | 1/8 | 3840 | 6000
P5 | SMD2727 | 320*160 | 64*32 | 1/8 | 3840 | 6000
P6.67 | SMD3535 | 320*160 | 48*24 | 1/6 | 3840 | 6000
P8 | SMD3535 | 320*160 | 40*20 | 1/5 | 3840 | 5500
P10 | SMD3535 | 320*160 | 32* 16 | 1/2 | 3840 | 5800
320x160mm with Flexible Mask Series Outdoor 06 LED Display Module

## Slide 45
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P4 | SMD1921 | 80*160 | 20*40 | 1/ 10 | 3840 | 5500
P5 | SMD1921 | 80*160 | 16*32 | 1/8 | 3840 | 5500
P6.67 | SMD3535 | 80*160 | 12*24 | 1/6 | 3840 | 5500
P8 | SMD3535 | 80*160 | 10*20 | 1/5 | 3840 | 5500
P10 | SMD3535 | 80*160 | 8*16 | 1/2 | 3840 | 5500
80x160mm Series Outdoor LED Display Module 06

## Slide 46
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P2.6 | SMD1415 | 250*250 | 96*96 | 1/24 | 3840-7680 | 4500
P2.97 | SMD1415 | 250*250 | 84*84 | 1/21 | 3840-7680 | 4500
P3.91 | SMD1921 | 250*250 | 64*64 | 1/8 | 3840-7680 | 6000
P3.91 | SMD1921 (black) | 250*250 | 64*64 | 1/8 | 3840-7680 | 4000
250x250mm Cable Connection Outdoor LED 06 Display Module

## Slide 47
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P2.6 | SMD1415 | 250*250 | 96*96 | 1/24 | 3840-7680 | 4500
P2.97 | SMD1415 | 250*250 | 84*84 | 1/21 | 3840-7680 | 4500
P3.91 | SMD1921 | 250*250 | 64*64 | 1/ 16 | 3840-7680 | 4800
P3.91 | SMD1921 | 250*250 | 64*64 | 1/8 | 3840-7680 | 6000
P3.91 | SMD1921 (black) | 250*250 | 64*64 | 1/8 | 3840-7680 | 4000
250x250mm Hub Connection Outdoor LED 06 Display Module

## Slide 48
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P2.6 | SMD1415 | 250*250 | 96*96 | 1/24 | 3840 | 4500
P2.97 | SMD1415 | 250*250 | 84*84 | 1/21 | 3840 | 4500
P3.91 | SMD1921 | 250*250 | 64*64 | 1/ 16 | 3840 | 4800
250x250mm Hub Connection Flexible 06
Outdoor LED Display Module

## Slide 49
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P3 | SMD1415 | 192* 192 | 64*64 | 1/ 16 | 3840 | 5500
P6 | SMD2727 | 192* 192 | 32*32 | 1/6 | 3840 | 5500
P6 | SMD3535 | 192* 192 | 32*32 | 1/8 | 3840 | 6000
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P3.79 | SMD1921 | 288*288 | 76*76 | 1/ 19 | 3840-7680 | 4500
P4.8 | SMD1921 | 288*288 | 60*60 | 1/ 10 | 3840-7680 | 4500
288x288mm Hub Connection Outdoor LED 06 Display Module
192x192mm Series Outdoor LED Screen Panel

## Slide 50
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P2.5 | SMD1415 | 160*160 | 64*64 | 1/ 16 | 3840 | 5000
P4 | SMD1921 | 256*128 | 64*32 | 1/8 | 3840 | 6000
P8 | SMD3535 | 256*128 | 32* 16 | 1/4 | 3840 | 6000
P10 | DIP346 1R1G1B | 160*160 | 16*16 | 1/4 | 1920 | 8000
P16 | DIP346 1R1G1B | 256*256 | 16*16 | 1/ 1 | 1920 | 10000
Other Series Outdoor LED Screen Module 06

## Slide 51
Model | LED Type | Module Size （MM） | Module Resolution | Driving Mode | Refresh Rate(Hz) | Brightness(Nits)
P2.5 | SMD1415 | 320*160 | 128*64 | 1/ 16 | 3840 | 5000
P3.076 | SMD1415 | 320*160 | 104*52 | 1/ 13 | 3840 | 5000
P4 | SMD1921 | 320*160 | 80*40 | 1/ 10 | 3840 | 5000
P5 | SMD1921 | 320*160 | 64*32 | 1/8 | 3840 | 5000
P6.67 | SMD3535 | 320*160 | 48*24 | 1/6 | 3840 | 5500
P8 | SMD3535 | 320*160 | 40*20 | 1/5 | 3840 | 5000
P10 | SMD3535 | 320*160 | 32* 16 | 1/2 | 3840 | 6000
P4 | SMD1921 | 80*160 | 20*40 | 1/ 10 | 3840 | 5500
P5 | SMD1921 | 80*160 | 16*32 | 1/8 | 3840 | 5500
P6.67 | SMD3535 | 80*160 | 12*24 | 1/6 | 3840 | 5500
P8 | SMD3535 | 80*160 | 10*20 | 1/5 | 3840 | 5500
P10 | SMD3535 | 80*160 | 8*16 | 1/2 | 3840 | 5500
320×160/80x160mm Energy-saving Series 06
Outdoor LED Display Module

## Slide 52
ANTIX